## Slide 1: Search, Navigate, and Actuate
Qualitative Navigation

## Slide 2: Navigation
Critical ability for mobility
Challenging, because strong coupling with:
Sensing, Planning, Acting
Hardware / Software architectures
Problem solving, computational efficiency

## Slide 3: Hierarchical Paradigm
Murphy, Figure 2.5

## Slide 4: Hybrid Paradigm
reactive
deliberative
Murphy, Figure 7.3

## Slide 5: Functionality needed for Mobility
Where am I going? Mission planning
What’s the best way there? Path planning
Where have I been? Map making
Where am I? Localization
Behaviors
Behaviors
Behaviors
Behaviors
deliberative
reactive
How am I going to get
there?

## Slide 6: Path Planning
What’s the Best Way There? depends on the representation of the world
A robot’s world representation and how it is maintained over time is its spatial memory
Two forms
  Route (or qualitative / topology)
  Map (or quantitative / metric)
Map leads to Route, but not the other way

## Slide 7: Route
Less general, but strong coupling with reactive layer
Attention points What features, landmarks to look for next
Distinction criteria What features are good to recognize places: - Have I ever seen it before? - What has changed since the last time?

## Slide 8: Landmarks
A landmark is one or more perceptually distinctive features of interest on an object or locale of interest
Natural landmark: configuration of existing features that wasn’t put in the environment to aid with the robot’s navigation (i.e. MacDonalds on the corner)
Artificial landmark: set of features added to the environment to support navigation (i.e. highway sign)
Highly useful landmarks are those visible at points where one has to select from multiple directions: gateways

## Slide 9: Coupling of landmarks
floor plan
relational graph
Nodes: landmarks, gateways,
goals
Edges: navigable path

## Slide 10: early relational graphs
Not coupled with how the robot would get there
Navigation path: direction and distance
Shaft encoder uncertainty accumulates

## Slide 11: Two solutions
Localization relative to the landmarks
Navigation path specified as sensor based behaviors

## Slide 12: Getting to a Distinctive Place: Neighborhoods
neighborhood
boundary
distinctive
place (within
the corner)
path of robot as it moves
into neighborhood and
to the distinctive place
Use one behavior until the landmark is seen then swap to a landmark localization behavior

## Slide 13: relational graphs with behaviors
Dead end
Follow-hall with Look-for-T
Follow-hall with Look-for-Dead-End
T-junction
Follow-hall with Look-for-door
Follow-hall with Look-for-T
Front door
Follow-hall with Look-for-T
Follow-hall with Look-for-door with Look-for-blue
Blue door

## Slide 14: Discussion
Advantages
  Eliminates concern over navigational errors at each node
  Robot can build up metric information over multiple trips, since error will average out
Disadvantages
  Features that are easy to recognize, are often too numerous to be unique
  Indoors it is nearly impossible to find distinctive places

## Slide 15: Class Exercise
Create a relational graph for this floor
Label each edge with the appropriate Local Control Strategy
Label each node with the type of gateway: dead-end, junction, room
Identify unique features of each node
Notes: Relational graph
Any Single Source Shortest Path Algorithm will work: see http://ciips.ee.uwa.edu.au/~morris/Year2/PLDS210/dijkstra.html
Russell: Uniform cost search (3.5 search strategies) (Mix between Breath-First and Best-First (sorting candidates on distance from source, but not using heuristic to estimate distance to goal).

## Slide 16: Alternative for relational graphs
Associative method
  spatial memory is a series of remembered viewpoints, where each viewpoint is labeled with a location
  good for retracing known paths

## Slide 17: Associative Methods
Create a behavior that converts sensor observations into ‘direction to go’ to reach a particular landmark
Assumption: location or landmark are:
  Perceptual stable: views from nearby locations look similar
  Perceptual distinguishable: views far away should look different

## Slide 18: Visual Homing
Partition image into coarse subsections (e.g., 16)
Each section measured based on some attribute – e.g., edge density, dominant edge orientation, average intensity, etc.
Resulting measurements yield image signature
Image signature forms a pattern
If robot nearby, should be able to determine direction of motion to localize itself relative to the location
Visual homing: the use of image signatures to direct robot to specific location

## Slide 19: Image Signatures
The world
Tessellated (like faceted-eyes)
Resulting signature

## Slide 20: Direction of movement

## Slide 21: QualNav
Basic idea: localize robot relative to particular orientation region
Orientation region: - multiple landmarks visible - Defined by landmark pair boundaries - Within an orientation region, all landmarks appear in same relationship
Vehicle localizes with view-angles, distances not used

## Slide 22: Example of orientation region

## Slide 23: Entering new orientation region

## Slide 24: Discussion
Advantages:
  Tight coupling of sensing to homing
  Robot doesn’t need to explicitly recognize what a landmark is
  Enables robots to build up maps as it explores
Disadvantages:
  require massive storage
  Require landmarks that are widely visible

## Slide 25: Applicable to RoboCup Soccer
  landmarks that are widely visible are available

## Slide 26: Route versus Map
How do humans find their ways? → Psychological data and theories
Human Landmarks != robotic distinctive places
Siegel & White’s hypothesis: landmarks → routes → map
Recently: landmarks & implicit map → routes

## Slide 27: Conclusions
Landmarks simplify the “where am I?” problem by providing orientation cues
Gateways: special cases of landmarks that allow robot to change directions
Distinctive places can be related to each other by local control strategies for traveling between them
Image signatures can be used to directly couple perception with acting