## Slide 1: Search, Navigate, and Actuate
Quantative Navigation

## Slide 2: Path Planning
What’s the Best Way There? depends on the representation of the world
A robot’s world representation and how it is maintained over time is its spatial memory
Two forms
  Route (or qualitative / topology)
  Map (or quantitative / metric)
Map leads to Route, but not the other way

## Slide 3: Spatial memory
World representation used by robot
Provides methods and data structures for processing and storing information derived from sensors
Organized to support methods that extract relevant expectations about a navigational task

## Slide 4: Basic functions of spatial memory
Attention: What features, landmarks to look for next?
Reasoning: E.g., can I fit through that door?
Path Planning: What is the best way through this building?
Recognition: What does this place look like? Have I ever seen it before? What has changed since I was here before?

## Slide 5: Quantitative spatial memory
Express space in terms of physical distances of travel
Bird’s eye view of the world
Not dependent upon the perspective of the robot
Independent of orientation and position of robot
Can be used to generate qualitative (route) representations

## Slide 6: Metric Maps
Motivation for having a metric map is often path planning (others include reasoning about space…)
Determine a path from one point to goal
  Generally interested in “best” or “optimal”
  What are measures of best/optimal?
  Relevant: occupied or empty
Path planning assumes an a priori map of relevant aspects
  Only as good as last time map was updated

## Slide 7: Metric Path Planning
Objective: determine a path to a specified goal
Metric methods:
  Tend to favor techniques that produce an optimal path
  Usually decompose path into subgoals called waypoints

## Slide 8: Configuration Space
Data structure that allows robot to specify position and orientation of objects and robot in the environment
Reduces # of dimensions that a planner has to deal with
Typically, for indoor mobile robots:
  Assume 2 DOF for representation
  Assume robot is round, so that orientation doesn’t matter
  Assumes robot is holonomic (i.e., it can turn in place)
  Classify “occupied” and “free” space

## Slide 9: Non-holonomic mobile robot
2D-surface in 3D configuration space

## Slide 10: Reduction and Discretization
6DOF
3DOF

## Slide 11: Object Growing
Since we assume robot is round, we can “grow” objects by the width of the robot and then consider the robot to be a point
Greatly simplifies path planning
New representation of objects typically called “forbidden region”

## Slide 12: Dilation of geometrical objects
Combination of straight walls and a round robot

## Slide 13: Minkowski sum
Take the union of the current (bit)map with a set of copies of a mask (circle for round robot) placed on the boundaries (edges) of the current shape.
Object dilation can make an environment description much more complex by making it smooth!

## Slide 14: Partitioning of free space
Decompose C-space into smaller (polygonal) cells

## Slide 15: Meadow map
A connectivity graph can be made cells, and a save path can be generated by travel the midpoint of the edges

## Slide 16: Problems with Meadow Maps
Not unique generation of polygons
Could you actually create this type of map with sensor data, instead of a-priori maps?
Uses artifacts like edges and corners of the map to determine polygon boundaries, rather than things that can be sensed
In principle, one likes to decompose in large and stable cells

## Slide 17: Voronoi diagram
A Voronoi diagram is generated by a retract, leading to a (n-1)-dimensional hypersurface
The paths have maximal clearance, and are not optimal

## Slide 18: Uniform cells
In bounded low dimensional C-space, one can overlay the map with a grid (sampling).
Make a graph by each seeing each coxel as a node, connecting neighbors (4-connected, 8-connected)

## Slide 19: Path Search algorithms
Wave-propagation ~ breath first

## Slide 20: Search backwards
Wave-propagation ~ force field

## Slide 21: Differential A*
Keep the costs and arrows, redo only nodes that are ‘pointing into’ new forbidden areas

## Slide 22: Conclusions
Mobile robot has to model the free space to plan paths
After discretization into cells with connectivity, graph search techniques can be applied
Before discretization, the parameter-space has to be reduced to degrees of freedom of the robot
The shape of the robot can be transferred to the environment by stamping
Heuristics are handy for search techniques, but branches have their value (do not prune)