## Slide 1: Network measurements on Grids
Hans Blom & Paola Grosso
UvA - AIR group
http://www.science.uva.nl/research/air/

## Slide 2: Our motivation
The questions:
Can network tests and measurements be conducted on the Grid?
Can network monitoring be performed on a Grid infrastructure?
And if so, what are the basic requirements for the Grid infrastructure and the testing application?
The reasons:
More and more infrastructure in Grids.
Network is a one of the parameter for scheduling Grid jobs
More details on the research:
http://vangogh0.uva.netherlight.nl/GridFTP-tests/Doc/Grid_and_network_tests.html

## Slide 3: A suitable Grid
Starting point: the definition of a set of requirements that describe a Grid suitable for network tests and measurements.
A Grid suitable for network tests contains computing elements equipped with the necessary network testing tools. The needed characteristics of the end nodes should be specifiable at the time the tests are submitted to the Grid.
A Grid suitable for network tests should allow for message passing mechanism between the components running on different machines.
  For example, handling Grid-specific security issues, such as user proxy.

## Slide 4: DAS2 and Globus
DAS-2 is a wide area distributed cluster:
  200 nodes (400 CPUs) at five location
  PBS batch system for distributed and parallel computing research
  Globus toolkit installed on all nodes for Grid research
Interconnections:
  Myrinet used for internal low-latency communication among nodes in the same cluster
  Ethernet connection among cluster, runs over SURFnet5
  Gigabit Ethernet at the UvA cluster for network tests
Application can run at multiple location (Grid-fashion) using the MPI implementation used by Globus (MPICH-G2)
  Together with the PBS queuing system and the MAUI scheduler

## Slide 5: GridFTP as test tool
We wanted to focus on the tool used by the Grid “user”: GridFTP.
GridFTP also usable for memory to memory transfers
A high-performance, secure, reliable data transfer protocol optimized for high-bandwidth wide-area networks.
Secure authentication is provided by the GSI (based on X.509 certificates)
  We use the certificates issued by the Dutch Grid Authority.
More information:
http://www.globus.org/datagrid/gridftp.html

## Slide 6: Test setup
UvA
Leiden
Utrecht
Delft
VU
Our setup is UvA-centric.
We run the tests from and to
the UvA nodes.
Vlan-A
The connection among sites is
100mbps, over SURFnet5 infrastructure.
Vlan-B
Test at 1gbps among Uva nodes.

## Slide 7: Test setup
Scheduler
Site-A pool
Site-B pool
A cron job every two hours submits a request to the Grid scheduler for a server node and a client node
The scheduler finds available nodes to act as senders and receivers.
Sender
Receiver
GridFTP runs as “user”, executing memory to memory test.
Receiver
Sender

## Slide 8: Job analysis
Is the Grid suitable for network measurements?
How can we classify our results?
1. Response of the Grid to job submission
  Prompt job
    It runs within a suitable time (<== concept of promptness)
  Delayed job
    It runs, but after the “prompt” window
    There were other jobs on the Grid that were occupying all available nodes
  Failed job
    There have been no nodes available or the test has not completed
2. Underlying network capacity:
  We know what is the available bandwidth, so not really interested in the result.
  Full bandwidth
  Limited bandwidth

## Slide 9: Bandwidth
No real variation in the GridFTP throughput… expected!
Few unavailability period when nodes are down.
Daily, weekly, monthly graphs (from RRDTool) avaialable at:
http://vangogh0.uva.netherlight.nl/GridFTP-tests/Results/Index.php
Daily plot
Monthly plot

## Slide 10: Grid promptness
The delay between job submission and job start time is the measure of the Grid response reaction.
Most of the jobs are started within 30 seconds from submission.

## Slide 11: Results
1.0%
0.1%
-
0.5%
Prompt/limited
3%
-
-
-
Delayed/limited
97%
100%
100%
100%
Delayed/full
99.0%
99.9%
100%
99.5%
Prompt/full
Delayed
Prompt
Failed
3.9%
1.2%
5.5%
7.3%
84.8%
92.7%
89.8%
87.3%
11.3%
6.2%
4.7%
5.4%
UU
TUDELFT
LIACS
VU
Busier sites ==> more delayed jobs
Statistics after three months of data:

## Slide 12: Conclusions
From here:
  Finding new Grids to test on:
    Validate set of requirements
    Validate test infrastructure
  Monitor transition from SURFnet5 to SURFnet6 on DAS-2.
  Move test to DAS-3 (?)
More information is available in:
  Project main web page:
  http://vangogh0.uva.netherlight.nl/GridFTP-tests/
Comments and suggestions?
grosso@science.uva.nl
jblom@science.uva.nl

## Slide 13: Backup slides

## Slide 14: Testing on the Grid
Some of the requirements needed to run tests on the Grid:
Out-of-box and arbitrary test generators should be usable
A tool consists of a sender (client) and receiver (server):
  Receivers/servers should be managed (started and stopped) by the test tool: servers cannot run constantly on the Grid.
  Ports for servers cannot be fixed:port might be already in use on assigned node
  Traffic senders/clients should be started synchronised
Managing of the testing tools (traffic generators) should be centrally organised:
  Independent from generator type
  Independent from inter-node communication (MPI, SSH)

## Slide 15: Test tool setup
Management
Tool
Inter-node communication.
(SSH, MPI)
Client
Wrapper
Traffic
Sender
Server
Wrapper
Traffic
Receiver
Test
Traffic
OS I/O

## Slide 16: Test procedure
The following are the test steps:
  Form sender/receiver pairs from the host set configuration
  Start receivers with wrapper scripts; store test output locally on the receiver node
  Run tests with synchronised start on all selected senders; use output from server wrapper script to set send parameters (such as receiver port)
  Stop receivers (will need process ids from the wrapper scripts)
  Collect and process receiver and sender test result stored at the nodes