## Slide 1: Optical networking research in Amsterdam
Paola Grosso
UvA - AIR group

## Slide 2: UvA AIR
Some new acronyms:
  UvA = Universiteit van Amsterdam
  AIR = Advanced Internet Research group
The AIR group, lead by Cees de Laat is a research group within the UvA Faculty of Science, Department of Informatics.
It is composed by 12 people, researchers and Ph.D students, plus a varying number of master and bachelor students.
More information:
http://www.science.uva.nl/research/air

## Slide 3: AIR research activities
There are three main research lines within the group:
  AAA - (Authorization, Authentication and Accounting)
    Integration of network control planes using AAA
    Integration of Grid middleware using AAA
    Management and control of generic AAA scenarios
  2. Optical Networking
    Modeling of Optical Exchanges
    Multi-domain path discovery
  3. GigaPort Next Generation
The activities of the group are not rigidly separated.
Group members work in more than one area, to create an consistent and complementary research line.

## Slide 4: GigaPort-NG
GigaPort-NG = GigaPort Next Generation

A project that:
focuses on research for the next-generation network and its implementation.
involves academic institutions (as the AIR group), government and private sector.
Main research lines within GigaPort-NG are:
  Optical networking techniques
  High performance routing and switching
  Management and monitoring
  Grids and access to Grids
  Test methodologies

## Slide 5: SURFnet
Current production setup:
  15 POPs connected by thirty 10 Gigabit per second lambdas
  135 institutions connected at gbps levels
  IPv4 and IPv6 connectivity
Notes: Description of SURFnet

## Slide 6: SURFnet6
A new packet-switching and optical network that will serve the academic network.
Native IPv4, IPv6 and Light Path Provisioning over a single infrastructure.
Managed via a single control plane
From 20 routed location to 2 routed locations
Notes: Description of SURFnet6

## Slide 7: SURFnet6 photonic layer
Common Photonics Layer (CLP) in SURFnet6
Each Dutch institute connected to SURFnet6 will be able to get 4 (in the next future 8) lambdas for research.
Innovation: connections between institutes will be created on the “fly” depending on the needs.

## Slide 8: Optical exchanges
An optical exchange is a peering location that allows for traffic to pass from one provider to another in a connection oriented manner.
NetherLight
  the open optical exchange located in Amsterdam is an integral part of both the SURFnet and SURFnet6 networks;
  SONET/SDH cross connect and Gigabit Ethernet switching facility for high performance access to connected networks;
  operational since 2002.

## Slide 9: Netherlight
DWDM
SURFnet
10 Gbit/s
SURFnet
10 Gbit/s
SURFnet
10 Gbit/s
Dwingeloo
ASTRON/JIVE
Prague
CzechLight
2.5 Gbit/s
NSF
10 Gbit/s
London
UKLight
Stockholm
NorthernLight
10 Gbit/s
10 Gbit/s
Geneva
CERN
Amsterdam
Chicago
IEEAF
10 Gbit/s
SURFnet
10 Gbit/s
New York
MANLAN
Notes: Drawing of Netherlight

## Slide 10: Amsterdam LightHouse: equipment
The UvA/AIR LightHouse is a lab for network research, that serves as:
  demonstration facility
  workplace for students
  flexible testbed
Operational since Sep. 2004
Currently two clusters available:
  Vangogh cluster
    9 dual processor 2.8 GHz XEON
    Gigabit connections
  Rembrandt cluster
    Dual 64 bits Opteron processors 2.0 GHz
    Gigabit and 10 GE connections

## Slide 11: LightHouse connectivity

## Slide 12: A new networking
Several kind of high bandwidth applications and users require us to think in a new way to the network and it setup.
Think of:
  Sensor Grids
  Computational Grids
  Data store Grids
  Visualization Grids
  Lambda Grids
How to satisfy the needs for “high bandwidths” on transient basis?
Optical Exchanges can provide the user with access to light paths.

## Slide 13: Open Optical Exchange
A user can “interface” to an optical exchange via Web Services.
The main question to answer is: what is access and what are the interfaces?

## Slide 14: What is a lightpath?
An optical (virtual) path between end points with guaranteed bandwidth and level of service (deterministic behavior)
Characteristics:
  It can span multiple administrative domains.
    How do you make different administrative domains talk to each other?
  It is “temporary”.
    How do you allow a setup and teardown of such path?
  It is application/user-driven.
    How do you empower the users to create such paths?

## Slide 15: GLIF
Global Lambda Integrated Facility

## Slide 16: “User owned” network
How to arrive to a “user owned” network?
From the network provider/administrator perspective:
  Identify the network resources that will be made available to the user
  Provide the higher level interfaces to the user
  Define and implement the lower level (control) of network component
  Coordinate the setup with other involved domains
From the user perspective:
  Know about which paths are available
  Make reservation for a path
  Extend/cancel reservation
Notes: What does it mean to provision a path. What are the components of such middleware?

## Slide 17: Looking around…
There are working and in development example in this area:
UCLP = User Controlled LightPath Provisioning
  CANARIE implementation of Lightpath Provisioning
  In production in their network since July 2004
  Three implementation from Canadian universities, all providing web services interfaces to the user
DRAC = Dynamic Resource Allocation Controller
A NORTEL implementation of control plane (works on Nortel equipment only)
PDC and PIN= Photonic Domain Controller and Photonic Inter-domain Negotiation
Developed at EVL (UIC)
Single domain and multi-domain user controlled light paths

## Slide 18: Resource Management
Our work: starting from “single domain”, single “optical exchange” resource management interface.
Our playground the Amsterdam LightHouse and NetherLight.
Definition of Resources and Services
  What is a resources?
  What is a service?
Definition of a single Reservation
  What defines a reservation?
    start and end resource
    start time
    duration of reservation
Definition of Reservation broker
  How to keep track of all the available resources and their current status and future availability?
Notes: Resource Management: what is it and how to accomplish it?

## Slide 19: Resource Management and Web Services
Web Services are the glue that puts all of this together:
Globus WSRF, Web Services Resource Framework: create, manage, and exchange information between Grid Services.
We are coming out in the next month with:
A WSDL interfaces to available procedures
The implementation of single domain user reservation system
An authorization policy definition, to determine which applications/users can setup paths
Notes: Web Services interfaces

## Slide 20: Network Elements
A first step is the control of the underlying network components that need to be controlled.
What defines a Layer1 network device, a Layer2 network device, …?
What are the properties and methods that each one exposes to the external users?
Notes: Network Elements virtualization

## Slide 21: Network Elements
Notes: Network elements concrete implementation

## Slide 22: AIR Web Service
First implementation now available:
  Deals with the control of the network elements present in the LightHouse:
  Force10 switch
  Glimmerglass photonic cross connect
  Python based: ZSI implementation of Web Services
More information on:
http://vangogh0.uva.netherlight.nl/AIRWebServices/WS-Intro.html
Notes: What we have right now and which future directions we are taking

## Slide 23: Future use cases
iGrid2005 and SC2005 natural venues to demonstrate our implementation.
“iGrid 2005 is a coordinated effort to accelerate the use of existing multi-10 Gbps international and national networks, to advance scientific research, and to educate decision makers, academicians and industry researchers on the benefits of these hybrid networks. Not as an isolated demo, but as the the underlying mechanism through which other demonstrators will make use of our resources.”
For iGrid2005 the current count shows 1/3 of the demos using dutch resources!

## Slide 24: Conclusions
Optical exchanges and Lambda Grids offer a new exciting way to think of networking.
Development to make this available to the users and the application is under way, in many research groups around the world.
In the Us the National Lambda Rail (NLR) will offer access to researchers to dedicated lightpaths. Is SLAC going to take advantage of this?
See you in Amsterdam!