## Slide 1: StarPlane: Application Specific Management of Photonic Networks
Paola Grosso
SNE group - UvA

## Slide 2: The usual suspects…
Three players in the game:
  the application
  the network
  the control plane (and the management plane)
… and a few questions:
App
Photonic
network
Mgmt
plane
Control
plane
How to get a topology that suits the need?
How to communicate with the mgmt plane/ control plane?
How to drive the changes in the network?

## Slide 3: The StarPlane approach
StarPlane is a NWO funded project with major contributions from SURFnet and NORTEL.
The vision is to allow part of the photonic network infrastructure of SURFnet6 to be manipulated by Grid applications to optimize the performance of specific e-Science applications.
StarPlane will use the physical infrastructure provided by SURFnet6 and the distributed supercomputer DAS-3.
The novelty: to give flexibility directly to the applications by allowing them to choose the logical topology in real time, ultimately with subsecond lambda switching times.

## Slide 4: Deliverables
The project will deliver:
1. the implementation of the StarPlane management infrastructure
2. the implementation of an intelligent broker service to handle high-level requests
3. the modification of a set of real applications to exploit the functionality of such a management plane
4. a library of standard components (protocols, middleware) to support and build new applications

## Slide 5: StarPlane applications
- Large ‘stand-alone’ file transfers
  User-driven file transfers
  Nightly backups
  Transfer of medical data files (MRI)
Large file (speedier) Stage-in/Stage-out
  MEG modeling
  Analysis of video data
Application with static bandwidth requirements
  Distributed game-tree search
  Remote data access for analysis of video data
  Remote visualization
Applications with dynamic bandwidth requirements
  Remote data access for MEG modeling

## Slide 6: SURFnet6
In The Netherlands SURFnet connects between 180:
  universities;
  - academic hospitals;
  - most polytechnics;
  research centers.
with a user base of ~750K users
SURFnet6 went into production at the beginning of 2006.
A hybrid network with:
regular Internet use
lightpaths with speeds up to 10 Gbps

## Slide 7: Common Photonic Layer (CPL)
Photonic portion for lightpaths:
- dark fiber network (6000Km) with Nortel DWDM and TDM equipment
5 rings
initially 32 lambdas (4x9)
later 72 lambdas (8x9)
Each lambda with up to 10gbps possible throughput

## Slide 8: StarPlane setup
5 clusters at 4 locations
Sites connected on ring 1 of the SURFnet6 network
A dedicated band, with up to 8 channels
Possibility of external connections to other lambda networks via NetherLight
i.e Interaction with other control planes

## Slide 9: DAS-3 architecture
The LAN connection to the University network, via Ethernet switches.
The WAN/StarPlane connection to CPL, via Ethernet “bridging” card in a Myrinet switch.

## Slide 10: DAS-3 clusters
 | LU | TUD | UvA | UvA-MN | VU | TOTALS
Head |  |  |  |  |  | 
* storage | 10TB | 5TB | 2TB | 2TB | 10TB | 29TB
* CPU | 2x2.4GHz DC | 2x2.4GHz DC | 2x2.2GHz DC | 2x2.2GHz DC | 2x2.4GHz DC | 46GHz
* memory | 16GB | 16GB | 8GB | 16GB | 8GB | 64GB
* Myri 10G | 1 |  | 1 | 1 | 1 | 
* 10GE | 1 | 1 | 1 | 1 | 1 | 
Compute | 32 | 68 | 40 (1) | 46 | 85 | 271
* storage | 400GB | 250GB | 250GB | 2x250GB | 250GB | 89TB
* CPU | 2x2.6GHz | 2x2.4GHz | 2x2.2GHz DC | 2x2.4GHz | 2x2.4GHz DC | 1.9THz
* memory | 4GB | 4GB | 4GB | 4GB | 4GB | 1084GB
* Myri 10G | 1 |  | 1 | 1 | 1 | 
Myrinet |  |  |  |  |  | 
* 10G ports | 33 (7) |  | 41 | 47 | 86 (2) | 203
* 10GE ports | 8 |  | 8 | 8 | 8 | 32
Nortel |  |  |  |  |  | 
* 1GE ports | 32 (16) | 136 (8) | 40 (8) | 46 (2) | 85 (11) | 542
* 10GE ports | 1 (1) | 9 (3) | 2 | 2 | 1 (1) | 15

## Slide 11: StarPlane architecture
Connection from each site to:
OADM (fixed) equipment -
Optical Add Drop Multiplexer
and the WSS -
Wavelength Selectable Switches- in the Amsterdam area.

## Slide 12: WSS
WSS will allow us to redirect a selected input color to the output fiber
This allows us to flexibly reconfigure the network according to the application demands.
Goal of StarPlane is sub-second switching, and topology reconfiguration.
ref Eric Bernier, NORTEL

## Slide 13: Driving the topology change
Topology examples

## Slide 14: Management & control plane
The answers to the initial questions:
How to communicate with the mgmt plane / control plane ?
Determine the APIs between the application and the management plane:
- web services
- job scheduler
How to get a topology that suits the needs ?
Investigate the topologies more suited to the the applications
How to drive the changes in the network ?
Determine the capabilities of the various network devices in the network (Myricom Ethernet bridge-card, Myricom 10G HBA, Nortel CPL)
How to make it all work ?
Integrate all of our work and eventually make it work seamlessly.

## Slide 15: Authorization models
U
R
A
user
authority
resource
U
A
R
1
2
3
4
Pull model
U
A
R
3
2
4
1
Agent model
U
A
R
1
2
3
4
Push/token model
- Who is authorized to make requests to
the StarPlane control plane?
- How will we handle the authorization
sequences?
Agent model and token model seem more suitable for StarPlane than others.
Research will focus on:
Integration of (generic) AAA with the mgmt plane;
Usage of tokens within the network.

## Slide 16: Conclusion
More information available at:
Terena poster session;
Project web site: www.starplane.org
Contact people at the UVA:
  Paola Grosso - grosso@science.uva.nl
  Cees de Laat - delaat@science.uva.nl
  JP Velders - jpv@science.uva.nl
  Li Xu - lixu@science.uva.nl
… plus collaborators at the VU, and SURFnet and Nortel.
Questions or comments?