## Slide 1: iGrid2005: a lambda networking facility
Paola Grosso
AIR/ UvA

## Slide 2: What is iGrid?
Lambda networking in the scientific community:
it is not just different services over different wavelenghts in the same fiber. It indicates the creation of dedicated and application-specific lightpaths.
iGrid 2005, the 4th community-driven biennial International Grid event, held in San Diego from Sep.26 to Sep.29.
An example of lambda networking:
Optical devices
  End user application that communicate w/o intermediate L2 or L3 services
High bandwidth utilization
  Applications with lots of data
Flexible and reconfigurable network setup
  Setup changed on the fly to accommodate varying lightpaths
International connectivity
  Connections to all demonstrator countries

## Slide 3: Closer look: layer2 infrastructure

## Slide 4: Closer look: layer3 infrastructure

## Slide 5: The UvA involvement
The UvA/SARA LightHouse was used during the workshop to provide connectivity to UCSD via NetherLight:
  To applications using cluster nodes located in Amsterdam
  To applications transiting via Amsterdam
Layer2 switches (Force10 E600 and Nortel ESR 8610) provided WANPHY connectivity to the remote sites and LANPHY connectivity for locally attached nodes.
Nortel ESR
Force10
NetherLight
StarLight Force10
iGrid Force10
Local
clusters
SARA
switch

## Slide 6: Some results
Many demos, just remembering some in their relation to lambda networking:
  Link-local addressing demo
    With its automatic configuration of end nodes showed a way to address reconfigurability
  Nortel/ UvA VM Turntable demo & Nortel/UvA Token Based AAA
    With its use of end-to-end completely optical setup showed the typical use of optical devices
  SARA Tiled Display demo, a throughput record breaker
    With its high throughput showed the need of dedicated path that are tuned to the application needs
… and all of them with a very international flavor.

## Slide 7: Conclusions
iGrid2005 (and SC|05 coming up) are learning experiences on the current status of lambda networking facilities.
An article focusing on the network setup will be part of the special edition magazine on the workshop.
What have we learned?
  A lot, but mostly the need for automatic light paths creations and resource reservation and brokering.
  See later presentation on RDF and Resource Brokering by Bert Andree.
Comments and questions:
grosso@science.uva.nl